## Slide 1
Connectivity
Vehicle Status
Speed Limit
Raspberry Pi 3
CAN
Kafka
MQTT
The Central Gateway

## Slide 2
Gateway: Input - Output
CENTRAL GATEWAY
VCU-S
INVERTER
Mobile App
Web App
(VSK)
MQTT
/display-topic
Kafka
/display-topic
CAN
Publish
MQTT
/spd-limit-topic
Subcribe
Subcribe
Subcribe
Publish
AI camera
CAN
Speed, Odometer, VCU Performance, Status (Brake, Side Stand)…
Battery voltage,
battery current,…
Traffic Sign detection
Set
Speed Limit
CAN

## Slide 3
Gateway: SW design
Approach 1: When there is new data, Gateway will publish immediately
Vehicle
Main Loop:
WaitForCAN() //WhileLoop
ReadCANMsg()
PublishToServer()
CENTRAL GATEWAY
MQTT/ Kafka
/display-topic

## Slide 4
Gateway: SW design
Approach 2: Multi-threading, one thread to read & store data, one thread to publish cyclically
Vehicle
Main Thread: //ReadCAN
While True:
waitForCAN() //WhileLoop
readCANMsg()
updateCentralData()
// As per Message Source
CENTRAL GATEWAY
MQTT/ Kafka
/display-topic
Side Thread 1: //PublishToServer
While True:
readCentralData()
publishToServer()
delay(Some delay)
CentralData
{
‘Speed’: 20,
‘Odo’: 100,
‘BattU’: 51,
….
}

## Slide 5
Gateway: SW design
CentralData
{
‘Speed’: 20,
‘Odo’: 100,
‘BattU’: 51,
….,
‘TrafficSign’: 0,
‘SpdLim’: 30,
}
Side Thread 2: //Read SpeedLimit
While True:
waitForMQTTmsg() //WhileLoop
readMQTTMsg()
updateCentralData() //SpeedLim
Side Thread 1: //PublishToServer
While True:
readCentralData()
publishToServer()
delay(Some delay)
Main Thread: //ReadCAN
While True:
waitForCAN() //WhileLoop
readCANMsg()
updateCentralData()
// As per Message Source
Side Thread 3: //Send CAN
While True:
sendCAN()
delay(Some delay)

## Slide 6
Gateway: Solved and Unsolved problems
Solved:
- Support for flexible data formats, data sources, transmission protocols.
- Multi-Threading programming.
Unsolved:
- Delay time in transmission.
- Data consistency in Multi-Threading software.
- Still not deeply understand MQTT and Kafka.